Product Information Sheet

Daycon Products Company, Inc.   16001 Trade Zone Avenue, Upper Marlboro, MD 20774

Local: (301) 218-1000  Toll Free: (800) 394-0019  Fax (301) 218-7191

This sheet is not a Safety Data Sheet (S.D.S.), nor does it satisfy the requirements to have one.  All information on this sheet is believed to be accurate, but no warranty is expressed or implied.  The product described herein is for use only by trained, professional, cleaning personnel.

DURASHIELD

Duranotic Aluminum and Metal Surface Protectant & Seal

Description:		Durashield is a protective coating for duranotic aluminum and other metal surfaces. It adds luster to the treated metal while protecting it from the weather and pollution. It is a silicone based formulation containing a low odor solvent, which makes it more pleasant to work with on indoor projects. Durashield provides protection up to 2 years on metal, depending on the climate and pollution in the area.

Benefits:

      - Easy to apply

      - Restores luster and depth of color to surface

      - Not oily or sticky; actually resists soiling

      - Prevents many paint and ink type graffiti material from sticking to surface

      - Not removed by water or most detergents

Specifications:

Appearance:			Clear Liquid

Color:		 		Colorless

Odor:				Mild Solvent

Use Dilution:			Ready-to-Use

Storage Stability:	   	Two years minimum in sealed container

Protective Clothing:	           	See Safety Data Sheet (SDS)

VOC’s, as is:			70%

Product Conformance:		Manufactured by an ISO 9001:2008 registered company.

Applications:		Protect duranotic aluminum around entranceways and windows.  Protect stainless steel, brass, copper, and other metals in areas such as elevators, escalators, etc.  Not for use on flooring.

Comments:		Do not use this product near flames, sparks, or electric arcs. Store in cool area and keep container tightly closed.  Do not smoke while using this product.  Do not use on vinyl, Pexiglas®, styrene, or lacquers.

Directions:		All surfaces should be cleaned and dried before application of DURASHIELD. Dampen an area of a clean cloth with a small amount of DURASHIELD and apply evenly to the metal surface. Allow to dry 5 – 15 minutes and buff out with a clean dry soft cloth.

Product Disposal: 	This product is non-hazardous material. Dispose of in accordance with local, state, and federal regulations. It is recommended that the high density polyethylene container and any corrugated packaging be recycled.

Packed:

| Packaging/Description | Item Code |
| --- | --- |
| Gallon (4 per case) | DURASHIELDGAL |

Date:		         November 19, 2015