Product Information Sheet

Daycon Products Company, Inc.   16001 Trade Zone Avenue, Upper Marlboro, MD 20774

Local: (301) 218-1000  Toll Free: (800) 394-0019  Fax (301) 218-7191

This sheet is not a Safety Data Sheet (SDS), nor does it satisfy the requirements to have one.  All information on this sheet is believed to be accurate, but no warranty is expressed or implied.  The product described herein is for use only by trained, professional, cleaning personnel.

FLEXCOAT

Urethane-Acrylic Floor Finish

Description:		Flexcoat is a urethane-acrylic floor finish specifically formulated to finish rubberized floors and synthetic all-purpose sport floors.  Flexcoat	 has excellent adhesion to all surfaces and has the flexibility needed to 	stand up to the wear created by multiple sporting events. Flexcoat exhibits outstanding shine and durability and may be burnished up to speeds of 3,000 RPM.

Flexcoat may also be used on Permagrain flooring, and Pirelli or rubberized tile by mixing one part Flexcoat with three parts water and then applying it to the surface with a Fast Finish Mop.  Once dry, the floor may be burnished.

Benefits:

- For rubberized and synthetic sport floors

- Resists traffic and wear

- Excellent adhesion to all surfaces

- Tough and flexible

- Will not discolor

- May be used with Ultra-High Speed

- May be used on Permagrain flooring

- May be used on Pirelli tile

Specifications:

Appearance:			Opaque liquid

Color:				White

Odor:				Ammoniacal

Total solids:			20% min.

Use dilution:			As is for all purpose synthetic sport floors;

1:3 for Permagrain and Pirelli Tile.

Coverage (First coat):		1500-2000 sq. ft./gal.

Coverage (Recoating):		2000 sq. ft./gal.

Storage stability:		Two year minimum in a sealed container.

Protective clothing:		See Safety Data Sheet (SDS)

VOC’s, % as is:			3.9

Product Conformance:		Manufactured by an ISO 9001:2008 registered company.

Directions:		1) Prepare the floor, first, by stripping and neutralizing the surface. Use Daycon G-Force,

Renegade, Hurricane or LOS to strip, and Daycon Ready to neutralize the surface. 2) For best results, use a white, nylon, finishing mop to apply product. Apply a thin coat of Flexcoat,allowing 20-30 minutes drying time, before adding second coat. DO NOT RECOAT UNTIL THE PREVIOUS COAT IS COMPLETELY DRY. Buffing will produce a beautiful finish. 3) Maintain Flexcoat daily by dust mopping, damp mopping or scrubbing, then buffing once the surface is dry.

Product Disposal: 	Dispose of in sewer or approved landfill in accordance with local, state, and federal regulations.. It is recommended that the high density polyethylene container and any corrugated packaging be recycled.

Packed:

| Packaging/Description | Item Code |
| --- | --- |
| Gallon (4 per case) | 662776 |

Date:			April 17, 2013